## Slide 1: The status of the ITER project
Marek Scholz
Instytut Fizyki Jądrowej PAN

## Slide 2
18/03/2015
IFJ Kraków
Outline
Introduction
Controlled thermonuclear fusion
Ways of implementing controlled thermonuclear fusion.
The European fusion reactor program
Status of the ITER project
Summary
The seminar used materials presented by D. Campbell during ITPA Diagnostic Topical Group Meeting, ITER HQ, 11/2016 & 10/2017
The views and opinions expressed herein do not necessarily reflect those of the ITER Organization.

## Slide 3
Figure 1.1: World primary energy consumption from 1991 to 2016 in milion tons oil
equivalent (Mtoe). Source: [BP. British Petroleum Statistical Review of World Energy, 2017. (Cited in sections 1.1.1, 1.1, and 2.4.2.2.)]
Introduction

## Slide 4
Fossil fuels:
Petroleum
Natural gas
Carbon
Alternative sources (not affecting the thermal balance of the planet)
Biomass;
Hydro;
Sun;
Wind;
Other (geothermal, tides, ...)
Alternative sources (affecting the thermal balance of the planet)
Nuclear energy (based on nuclear fission)
Solar energy from space
Nuclear energy (based on nuclear fusion) - thermonuclear energy
Remark
Large-scale (global) energy requires:
Continuity of energy supply;
Network parameters guarantee
Introduction

## Slide 5
IFJ Kraków
The difference between the demand for energy and the possibilities of energy based on conventional energy sources
This can be the basis for the development of thermonuclear energetics
Bilion barrel of oil energy equivalent/y
Introduction

## Slide 6
18/03/2015
IFJ Kraków
Thermonuclear reactor fuel
Isotopes of hydrogen
hydrogen - 1H
Deuterim - 2H (0,016% in hydrogen)
Trytium - 3H (radioactive T1/2 = 12.262 lat, (1 – 150)·10-18 in hydrogen)
Helium
In nature 5 – 10%
4He – 99.999862 %, residual 3He
Large amounts on the moon
The problem of fuel for a thermonuclear reactor: very little tritium in nature (world stock of 20 kg) - a reactor using a mixture of deuterium and tritium will have to produce tritium from lithium
Lithium
In the Earth's cortex 6.5·10-3 %
~10% 6Li, ~90% 7Li
Fuel consumption for all of today's energy
D ~ 300 t/rok (5·1013 t in water);
Li ~ 10000 t/rok (5·1013 t )

## Slide 7
Status of projects
Two main ways - two methodologies :
Inertial Confinement Fusion (ICF):
  NIF (USA)
  Laser Megajoule (Francja)
Magnetic Confinement Fusion (MCF):
  ITER (Chiny, Indie, Japonia, Korea Pd, Rosja, UE, USA)
7
Methods of a plasma confinement
T ~ 28 keV; (nf0t)min  31019 m-3s
(D,T)
(1 keV = 1.1606107 oK ~ 107 oK)

## Slide 8
International
Thermonuclear
Experimental
Reactor
Power: 0,5GW
Time: 1000s
DEMO
DEMOnstration
Power Plant
Power: 2GW
Time: con.
Energy Production
Scaling
Notes: 8

## Slide 9
Basic parameters:
- Torus radius:…..3.1 m
- Chamber:H=3.96 m x S=2.4 m
- Plasma volume:…80 m3
- Plasma current:…..up to 5 MA
- Magnetic field: up to 4 T
1973 – decision about construction
1983 – getting started
The most important JET results :
1991:
The first controlled fusion with
D+T ~ 2MW during 1s was obtained
1997:
16MW fusion power was obtained 75% efficiency
Joint European Torus (JET)
10 keV
Line of magnetic field
Notes: 9

## Slide 10
Test of the necessary technology;
Test of materials for thermal and radiation load;
Demonstration of the possibilities of energy production from thermonuclear fusion
Basic Parameters:
- Torus radius:…..6.2 m
- Plasma volume:…300 m3
- Plasma current:…..do 15 MA
- Magnetic field: up to 5,3 T
- Pulse:………..up to 1000 s
- Power:…do 0,5 GW
- Efficiency:.………..up to 10
ITER
Notes: 10

## Slide 11
JET and ITER
Be first wall
700 m2
Tungsten
100 m2
Graphite CFC
50 m2
500 MW
16 MW
ITER
JET
11
Pf
Yn
- (50% neutron branch)
- (55% neutron branch)
- (4% neutron branch)
- (50% neutron branch)

## Slide 12
Major Project
Major projects related to thermonuclear power engineering
ITER
International Thermonuclear Experimental Reactor
In Europie
IFMIF/EVEDA:
International Fusion Materials Irradiation Facility/
Engineering Validation & Engineering Design Activity
In Japan
Published with permission of IFMIF-EVEDA
STP – satellit program associated with JT60SA
IFEREC – computer center, cooridnation center for DEMO R&D

## Slide 13
Component test
superconducting magnets
tritium delivery systems
PFC
remote maintenance
heating systems
security
Reactor blanket test
Construction materials
Blanket tests at
ITER
Maintaining plasma
Control of admixtures stability
Fuel and ash control etc
Technology (R & D)
Plasma Physics (R & D)
ITER
DEMO
IFMIF
Thermonuclear power plant
Main projects R & D
Notes: 13

## Slide 14
Plans and reality

## Slide 15
ITER differs in an important way from other devices:
  the experimental programme is determined by the need to reach high current and to demonstrate baseline fusion power as soon as possible
  Disruptions must be absolutely be mastered to reach high Ip
  to a large extent the whole of PFPO and a large fraction of the first part of FPO is ‘commissioning with plasma’ of all tokamak and plant systems for to prepare the reliable operation required to reach high Q
  nevertheless, we anticipate that even during the ‘commissioning with plasma’ phase in PFPO, that ITER will give access to many new aspects of fusion plasma research as the programme develops plasmas with parameters well beyond those which can be attained in present experiments
Research Plan: An Important Note

## Slide 16
During 2015 – 2016, the project has performed a ‘bottom-up’ analysis of the construction and operations schedule to develop a fully consistent programme towards plasma operation and fusion power production:
Schedule and IO-CT resource estimate to First Plasma consistent with Members’ budget constraints
4-stage operations programme developed towards fusion power production in DT, starting in late-2035
Baseline Schedule - ‘Staged Approach’
DT Operation
Stage I
Stage II
Stage III
Stage IV

## Slide 17
Pre-Fusion Power Operation (PFPO):
  First Plasma: nominal 100 kA/100 ms
  plasma operation to ~3.5 MA to establish initial divertor operation
  disruption loads, disruption detection, avoidance and mitigation
  extensive control and protection system commissioning
  development of plasma operation to ~7.5 MA/ 2.65 T (possibly ~10 MA/5.3 T)
  possible option for operation at 5 MA/1.8 T (early H-mode access) with ECRH and ICRF heating systems
  H-mode operation and ELM Control (helium/ hydrogen?)
  options for long pulse operation in L- and H-mode
  demonstration of 15 MA/ 5.3 T operation
  PWI programme: eg, fuel retention/removal, dust, limiter/divertor heat loads
Research Plan Structure and Activities I

## Slide 18
Fusion Power Operation (FPO):
  development of deuterium H-modes and preparation of DT scenarios
  trace tritium experiments to initiate transition to full DT operation
  development of 15 MA/5.3 T DT scenario
  initial DT operation to short-pulse (few×10s) several 100 MW fusion power
  optimize Q with target of Q ≥ 10 to few×10s
  develop scenarios for long-pulse operation:
    Inductive: Q ≥ 10 towards ~500 s
    Hybrid: Q ~ 5 (up to 10, if possible) towards ~1000 s
    Non-inductive: Q ~ 5 towards ~3000 s
  PWI programme: Fuel retention/ removal, material migration, heat loads/ detachment control
Research Plan Structure and Activities II

## Slide 19
Overview of ITER Experimental Plan

## Slide 20
PF Coil Facility
IO Headquarters
Tokamak Complex
Construction underway
Assembly Hall
Being equipped
400 kV switchyard
Cryostat Workshop
Storage area 1
Batching plant
Cryoplant
Construction underway
Cleaning facility
Construction underway
(Aerial Photo October 2016)
Worksite progress
Transformers
Service Building
Radiofrequency Bdg
Construction underway
Cooling Systems
Construction underway

## Slide 21
Tokamak Complex

## Slide 22
Tokamak Complex
Oct 2018

## Slide 23
Tokamak Complex

## Slide 24
Plant Systems provided by F4E
Remote Handling Systems
Cryogenic Systems
ICRH Antenna & Components
ECRH Launchers & Components
Neutral Beam Heating
12 Diagnostic
Systems
Test Blanket Modules

## Slide 25
F4E Contributions to ITER: First Wall
215 First Wall Panels
  IBERDROLA-LEADING-WOOD
  FRAMATOME
  ATMOSTAT