## Slide 1: LNL accelerator facilities
Luca Bellan
on the behalf of INFN-LNL

## Slide 2: Index
Overview of the National Laboratories of Legnaro accelerators
  Existing accelerators, stable ion production and acceleration for user
Light ions facilities
  CN
  AN2000
Heavy Ions Facility
  TANDEM ALPI PIAVE
General accelerator operation overview
Upgrades
Contacts

## Slide 3: Accelerators
The LNL accelerators for users supply light and heavy stable ions in the order of 10 MeV/u.
Electrostatic type accelerators
RF (superconductive) type linac accelerators
Nuclear Physics experiments
Applied Physics: neutron experiments, medical and industrial applications, accelerator developments
High intensity linac (RFQ IFMIF, DTL ESS, Anthem)
Irradiation lines for material tests for industries and users.
Cyclotron and new normal conductive RFQ
SPES: Radioactive Ion Beams
for users
under development

## Slide 4: Light ions facilities
Electrostatic type

## Slide 5: CN
Van der Graaf accelerator type. Light ions up to 6 MV terminal voltage.
Used for applied physics and nuclear physics experiment
Neutron irradiation experiments.
Pulsing system at 3 MHz is available

## Slide 6: Neutron flux irradiation
[0] Selva et al, 2022, “Microdosimetry of an accelerator based thermal neutron field for Boron Neutron Capture Therapy” Appl. Radiat. Isot. 182, 110144”
[1] Agosteo et al, 2011, “Characterization of the energy distribution of neutrons generated by 5 MeV protons on a thick beryllium target at different emission angles.”, Appl. Radiat. Isot. 69, 1664”
MUNES line
  The line is equipped with a graphite heavy water thermal neutron moderator that generates a neutron flux of 4.5×105 n/(s·cm2), 96% fraction [0,1]
  Test of the composite target material: blistering, resistance to power deposition (up to 3 kW/cm2, beam spot 1 mm radius)
0 Line: can be equipped with Li target or Be target.
  In the latter case, we can reach a neutron flux (5 MeV protons, 3 uA) of 4.5×109 s peaked at 1.2 MeV, with maximum 3.2 MeV.
  Can be equipped with different moderators.
Courtesy of Anna Selva. anna.selva@lnl.infn.it
Test of neutron converter for accelerators, materials

## Slide 7: AN2000
Van der Graaf accelerator type. Light ions with 2 MV terminal voltage
Used for applied physics and nuclear physics experiment
Microbeam experiments

## Slide 8: AN2000 - microbeam
Ultra low intensity (100-1000 p/s) ion beams rastered on the DUT
APPLICATIONS
► 2D detectors efficiency maps
► localised irradiations
Iron yoke cut from single piece, accuracy <2µm
Accurate hyperbolic pole tips
Undetectable 6-pole field contamination
Nucl. Instrum. Meth. B54 (1991) 52-63
Courtesy of Valentino Rigato and Matteo Campostrini – valentino.rigato@lnl.infn.it

## Slide 9: Accelerator components tests AN2000
Beam based alignment of the new SPES diagnostics
Relation between the centre of the wire and the actual position of the beam
Courtesy of Pierfrancesco Mastinu
AN2000 beam
collimator
Detector and readout

## Slide 10: Heavy ion facility
RF type*
*Tandem type accelerator also

## Slide 11: Tandem-ALPI-PIAVE facility
ALPI
CW Folded independent cavity linac
Design and built 80’-90’
One of the first prototypes in Europe.
82 QW cavities at 4 K
  80 MHz low beta (0.047, 0.055)
  160 MHz medium beta (0.11)
  160 MHz high beta (0.13)
Output energy ions of about 10 MeV/amu

## Slide 12
TANDEM
ALPI
Tandem XTU accelerator
14 MV terminal voltage
Negative ion source
Up to light-medium A (around 50) for ALPI injection
Highest energies output for light ions, 22 MeV/u
Tandem-ALPI-PIAVE facility

## Slide 13: Tandem-ALPI-PIAVE facility
TANDEM
ALPI
PIAVE
PIAVE superconductive RFQ
Medium –heavy mass, 50 < A < 208
External buncher three harmonics , two RFQ cavities (80 MHz) with /4 inter-tank distance
ECR nanogan ion source

## Slide 14
TANDEM
ALPI
Up to hundreds nA, max A/q = 8 (NO SC issue whatsoever, problem on the applied fields)
From C to Pb (to U) and stable isotopes.
PIAVE
Tandem-ALPI-PIAVE facility

## Slide 15: A decades of upgrades to accelerate heavy ions at higher energies
- 2022
- 2018
- 2013
- 2010-11
ALPI beams, from TANDEM and PIAVE
Drop in energy output in 2023 is due to no experiments requested at 1300 MeV.
under authorization procedure.

## Slide 16: Towards heavy ions
- 2010
- 2018
- 2022
- (exp. in 2024) – Authorization ongoing
- 2013

## Slide 17
Test on PIAVE LEBT of new beam profiler
Installed new diagnostic box for testing accelerator components:
Test of RIB profiler signal and RIB robustness
136Xe18+ @ 2.23 MeV, I = 1.3 uA, 3 W
Possible to ramp up to 8 MeV, 2 uA, 16 W.
0.98-1.1 mW (interceped power on the central wire)
Accelerator components tests TAP - 2

## Slide 18
Test on ALPI of FFC for longitudinal beam measurements
The beam was 18O6+ at 100.26 MeV, 100 nA from TANDEM.
The 80 MHz buncher AL.HEB.01 was used in order to focus the beam longitudinally at test BOX diagnostics (which contains the FFC)
Accelerator components tests TAP - 3
FFC
Buncher 80 MHz
Test box

## Slide 19: Irradiation for industries
First irradiation service for private company successfully tested before summer 2023.
A 136Xe beam was accelerated with PIAVE-ALPI complex up to 1 GeV energy and sent to SIRAD irradiation chamber.
Flux dosimeter and uniformity calibration was performed by 2 boards hosting 4 silicon diodes each.
Average beam flux was about 2 x 103 ions/cm2/sec and total accumulated flux was 1 x 107 ions/cm2 in 8.3 min exposure.
LET = 89.5 MeV cm2/mg
Courtesy of Jeff Wyss, wyss@unicas.it

## Slide 20: General overview

## Slide 21: Experiments - overview
Applied physics:
Surface studies (sputtering characteristics)
Irradiation for material/components testing
Medical physics
Radiological studies
Accelerator tests:
Accelerator improvement studies
Experimental run feasibility studies
Diagnostics and accelerators components tests
High level application tests.

## Slide 22: Accelerators overview
Chart: YEAR
| 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023(dec)
Beam on Target | 2826.5 | 3027.5 | 3253 | 3849.5 | 2910 | 792 | 2253.5 | 528 | 674 | 719 | 2560 | 3831.5
Beam Preparation | 244 | 360 | 704 | 230 | 180.5 | 131 | 491 | 423.5 | 93 | 96 | 541 | 1138
Accelerator Division Tests | 224 | 0 | 174 | 240 | 132 | 360 | 24 | 313 | 48 | 0 | 240 | 214
Unscheduled Maintenance | 441 | 786.5 | 132 | 293 | 355 | 2241 | 1216 | 2686.5 | 576 | 72 | 461 | 229

## Slide 23: Upgrades

## Slide 24: Tandem-ALPI-PIAVE – Normal conductive RFQ
TANDEM
ALPI
SPES RFQ: normal conductive 4-vane internal bunching RFQ
coupled with SPES Charge-Breeder (ECRIS type) and MRMS
Higher energy injection to ALPI, 727 keV/u VS 587.5 keV/u (PIAVE)
Optimized longitudinal emittance output
Higher RFQ transmission: 93% SPES vs 55% PIAVE
SPES RFQ
PIAVE

## Slide 25: SPES upgrade
Use of existing superconductive linac ALPI to post accelerate the RIBs
Radioactive ion beams input through the SPES RFQ
AGATA
AGATA: HPGe detector array

## Slide 26: SPES upgrade
AGATA
ADIGE
ISOL target
Cyclotron
Cyclotron: 30-70 MeV H+, 800 uA
Target: UCx target ISOL type
ADIGE: post acceleration and charge breeding line
AGATA: HPGe detector array

## Slide 27
AGATA
ADIGE
ISOL target
Cyclotron
Cyclotron: 30-70 MeV H+, 800 uA
Target: UCx target ISOL type
ADIGE: post acceleration, medium mass sepration and charge breeding line
AGATA: HPGe detector array
SPES upgrade

## Slide 28: Cyclotron
Normal conductive cyclotron with double extraction lines (70 MeV protons at 800 uA). It is under commissioning, and it will be equipped with eight target stations. Main stations here
LARAMED: research on medical radionucleotides
ISOL 1 & 2 : SPES and other activities

## Slide 29: CN – irradiation upgrade
BEAM FEATURES:
  Monochromatic Beams: 1H+, 4He+
  Energy: 0.2÷5.5 MeV
  Standard Beam Size: 2÷8 mm (FWHM)
  Beam Current: 1-400nA (typical)- (400nA - 2μA energy dependent)
IRRADIATION SPECIFICATIONS OF THE NEW FACILITY
  Large area uniform irradiation of spacecraft materials and components in a wide range of energies and fluences
    Fluence: 1x109 ÷ 1016 cm-2
    Energy: 0.2÷5.5 MeV
  Large area
    ΔX·ΔY=20x20cm2 @ 2 MeV, ΔX·ΔY=8·8cm2 a 5.5 MeV
    XY beam scanning
  Uniformity
    Spatial uniformity: target ≤ ±1%
  Accuracy
    Accuracy: base ≤ ±5% - target to ≤ ±3% (multiple Faraday cups)
  No Carbon build-up (cryogenic LN2 trap)
  Time for full irradiation
    From 30s to several hours
  Certification of irradiation: ESA/ASI ongoing
Courtesy of Valentino Rigato and Matteo Campostrini – valentino.rigato@lnl.infn.it

## Slide 30: AN2000 – line upgrades
beam
DUT holder
ΔY travel: 100mm, bi-direct. repeatability ±50 nm
ΔZ travel: 50mm, bi-direct. repeatability ±50 nm
ΔX travel: 150mm, bi-direct. repeatability ±2 µm
Collimator holder
Parallel-kinematic design for six degrees of freedom (X, Y, Z, θX, θY, θZ) for collimator precise alignment with ion beams
Chamber at 0° beam-line at AN2000
Low divergence ion beams
Vibration free pumping system
Water with temperature control (±0.5°C)
Vacuum: ≤1x10-7 mbar
APPLICATIONS
► Shoot single ions in precise position (Zi,Yi) in ΔZ, ΔY steps
  2D array of individual defects
  Single photon sources (eg.: QUANTEP)
► Vary the energy keeping the DUT-collimator relative position fixed
  Individual centers in 3D (Zi, Yi, Xi)
► Vary ion specie at same (Zi,Yi) position: creation of totally new color centers / defects with multiple single ion implantation in semi and super conductors
► Localized irradiation of nano-wires and band engineered low-D materials(IV, III-V) (QUANTUM SENSING and METROLOGY, PHOTONICS)
Courtesy of Valentino Rigato and Matteo Campostrini – valentino.rigato@lnl.infn.it

## Slide 31: Contact information:
Accelerator Division (beam requests and questions)
enrico.fagotti@lnl.infn.it – Accelerator division head
giovanni.bisoffi@lnl.infn.it
luca.bellan@lnl.infn.it
PACbeams@lnl.infn.it (information about beams, species energies)