## Slide 1: Enabling controlled nuclear fusion – the role of magnetic diagnostics in tokamaks
André Torres
Prepared for the Seminar for Young Researchers
26th March 2026

## Slide 2: A fundamental difference…
Equilibrium
Stability
Magnetic confinement
Confinement
time
Plasma temperature
Density
Nuclear fusion
‘triple product’
Nuclear fission
Nuclear fusion
“The reactivity that generates power either goes up [holds up a red card] or it goes down [holds up a blue card].”
Chernobyl (2019, HBO)
In magnetic confinement nuclear fusion, the reaction does not occur naturally, we need to create – and maintain – the conditions for its existence.

## Slide 3: In this presentation…
Principles of the tokamak
The magnetic diagnostic system
Types of sensors
What is their role?
Development of the diagnostic for COMPASS-U
Challenges and R&D
Sensors
Low drift signal integration for COMPASS-U
Real-time ELM detection for buffering
The magnetic diagnostic is intrinsically linked with the operation of the magnetic confinement device.
It is present since the early devices,
and a fundamental tool for plasma both physics research and for power-plant operation.

## Slide 4: The vessel for magnetic confinement
[1] J. P. H. Goedbloed and S. Poedts, Cambridge University Press, 2004
[2] Online: R. Nave, HyperPhysics, 2017
[1]
[2]
tritium
He-4
Li-7
(fast) neutron
(slow) neutron
Breeding blanket
Tokamak (from toroidalnaja kamiera s magnitnymi katuszkami)
Toroidal field coils create a strong toroidal field
Current is induced on the conductive plasma (secondary of a transformer)
The plasma current generates a poloidal field
The resulting field lines are helical, which compress the plasma
Balance between the kinetic and magnetic pressures → Equilibrium
Important definitions!
Witvoet, et al., Nuclear Fusion, 2009

## Slide 5: Where are the particles?
Particles follow the helical field lines, gyrating with a Larmor radius
They are confined along the flux surfaces, from the core to the Last Closed Flux Surface, where the field lines start being open
Magnetic surfaces of same poloidal (magnetic) flux - Ψ

## Slide 6: Magnetic equilibrium
Grad-Shafranov equation
Internal balance between the plasma pressure and the magnetic field forces. Gives rise to the shape and position of the plasma, controlled by the currents in the external coils.
Hot plasma tries to expand
Lorentz force compresses the plasma
R, Z – 2D coordinates p(ψ) – pressure profile F(ψ) – toroidal field profile
Ψ is both the dependant and independent variable! Would be really convenient to measure it!

## Slide 7: Optimizing the tokamak: elongation
We want to drive more current in the same volume, with a fixed major radius. Beyond a certain point, massive instabilities appear.
Elongation increases the cross section of the plasma allowing longer trapped particle paths.
G.D. Tommasi, 2019
Problem: Elongated plasmas are vertically unstable!
Solutions:
Eddy currents on conductive structures
Real-time magnetic control
M. Walker, General Atomics

## Slide 8: Optimizing the tokamak: the divertor
Where does the plasma ‘end’?
The closest metallic structure will act as a limiter – closed field lines (confinement) inside, open field lines outside.
Problem: Plasma exhaust is concentrated on the limiter
S. Krasheninnikov, A. Smolyakov & A. Kukushkin - Edge Plasma Issues in Magnetic Fusion Devices
Solution: Divertor
  Withstands the high alpha particle heat flux
  Away from the plasma core
  Pumps out impurities
COMPASS – Carbon divertor
WEST – Tungsten divertor
Photos: IPP-CAS, CEA

## Slide 9: Optimizing the tokamak: H-mode
H-mode is an operating regime with enhanced confinement (higher confinement time) reached through the addition of external heating. It is characterized by the formation of a transport barrier at the edge, appearing as a pedestal in the radial profiles.
F. Jaulmes, et al., PhDiaFusion, 2021
J. W. Connor et al, AIP Conference Proceedings 1013, 174-190 (2008)
High confinement mode

## Slide 10: The modern tokamak
ITER
Under construction in France
~20 B EUR
In-kind contributions form 7 members
Aim of demonstration of net positive energy production with Q=10
Person

## Slide 11: The magnetic diagnostic

## Slide 12: Magnetic diagnostic – Principle of operaton
Adapted from: J. Wesson, Oxford Univ. Press, 2011
Magnetic probes (Mirnov coils) ➡ Local B Flux loops ➡ Loop voltage (Vloop), poloidal flux (ψ) Rogowski coil ➡ Plasma current (Ip) Diamagnetic loop ➡ Plasma energy (W) Saddle loops ➡ Radial Magnetic field BR
Inductive magnetic sensors
Adapted from the XKCD comic
https://imgs.xkcd.com/comics/dependency.png
Some wires around the device
Physics exploitation on tokamaks and stellarators

## Slide 13: Rogowski coil
Main measurement for plasma current!
Essential for physics exploitation and control alike
In addition, used to measure other currents such as in the Vacuum Vessel
E. Matveeva, 2019
P. Moreau, et al., “Prototyping and testing of the continuous external rogowski ITER magnetic sensor,” 2013

## Slide 14: Magnetic probes (Mirnov coils)
Max
Max
Min
Min
m=2
T. Hender, et al., Nuclear Fusion, 2004.
TM-3 1964
DIII-D 1986
E. J. Strait, 2008
Provide local B measurements
Main tool to study the Magneto-Hydro-Dynamics (MHD) of the plasma, i.e. deviations from the equilibrium state
In addition to physics, we can monitor and prevent the growth of instabilities that could lead to an abrupt termination of the discharge
Control plasma shape and position

## Slide 15: Flux loops
Flux loops also have two useful interpretations:
Loop voltage of the plasma
  Primary mechanism for driving current
  Essential for the gas breakdown
  Plasma resistance ->
  Monitoring to prevent disruptions
  Ohmic heating power
X and divertor strike points
  With measurements outside the plasma we obtain the main plasma core parameters
Poloidal flux

## Slide 16: Saddle (siodło) loops
Shaped like a saddle because they sit on the surface of the VV, torus-shaped
Sensitive to radial flux, averaged over a large area
On a phi-theta map, they are a rectangle
The signal can be interpreted as:
φ1
Δϕ
φ2
Extremely important to detect low frequency MHD modes, specially non-axisymmetric non-rotating modes
Toroidal
Poloidal

## Slide 17: Diamagnetic loop
Main measurement of the plasma energy (W)
The diamagnetic flux is the difference between the total toroidal flux with plasma and that in the absence of plasma (vacuum flux).
The vacuum flux is determined either by measuring the current flowing in the toroidal field coils or, equivalently, the toroidal field outside plasma column.
Challenging measurement because the toroidal flux is several orders of magnitude larger than the diamagnetic flux
Gernhardt, et. al, Design and electronic compensation of a diamagnetic loop and its applications in the ASDEX tokamak, Tech. Rep., 1986
Approximation for elongated plasma

## Slide 18: Applications (ITER)
Vayakis, 2012

## Slide 19: Magnetics for COMPASS Upgrade

## Slide 20: COMPASS Upgrade
COMPASS-U will be a compact and flexible device with a set of unique parameters to support the ITER operation and address key challenges of DEMO reactor design. In particular:
Power exhaust and liquid metal concepts
Alternative confinement modes and plasma shapes
“Hot-wall” operation: vacuum vessel can be heated up to 300 ºC and later 500 ºC
These are enabled by:
Cryogenically cooled copper coils
Metallic first wall (full metallic device)
Replaceable top and bottom divertors
High heat fluxes
NBI + ECRH heating
Major radius R = 0.894 m
Minor radius a = 0.27 m
Aspect ratio A = 3.3
Triangularity δ ∈ 0.3-0.6
Tor. mag. field Bt ≤ 5 T
Plasma current Ip ≤ 2 MA
Elongation κ ≤ 1.8
Pulse length t ∈1-3 s
(11 s max.)
Vondracek, et. al, Preliminary design of the COMPASS upgrade tokamak, Fus. Eng. Des., 169, 2021
Main parameters:

## Slide 21: COMPASS-U magnetic sensors
Detect fast oscillations:
2 poloidal arrays
4 toroidal arrays LFS
2 toroidal arrays HFS
1 poloidal array TPC+Hall
Measure vacuum vessel currents:
1 poloidal array Inner Partial Rogowski
1 poloidal array External partial Rogowski
1 internal full rogowski coil
1 external full rogowski coil
24 current shunts
2 segmented rogowski coils under PSP
1D MIC Eq. coil
Stainless steel sheath (SS316)
Ceramic powder (MgO)
Conductor (Cu)
Mineral Insulated Cable (MIC)
Survivability of more than 700 oC
Shields high-frequency signal
Image: nVent
Magnetic equilibrium:
2 poloidal arrays of MIC coils (1D, 2D)
4 Diamagnetic loops (two with compensation windings)
1 Full Rogowski
1 poloidal array of partial rogowski coils
30 poloidal flux loops
Over 500 individual sensors planned, redundancy included. Approx. 3 km MIC
How much does the MIC attenuate the magnetic signal? At which frequencies?

## Slide 22: MIC sensor prototyping and optimization
A. Torres, et al., Mineral insulated cable assessment for inductive magnetic diagnostic sensors of a hot-wall tokamak, JINST, 2019
Torres, K. Kovarik et. al, Test bench for calibration of magnetic field sensor prototypes for COMPASS-U tokamak, Fus. Eng. Des., 168, 2021
MIC
non-MIC

## Slide 23: Magnetics Data Acquisition Electronics

## Slide 24: Magnetic diagnostic – integration
Non-inductive magnetic sensors:
Current shunts ➡ Currents in passive structures Hall probes ➡ Local B FOCS1 ➡ Plasma current (Ip) MSE2 ➡ B pitch (q(r)) 1 Fiber Optic Current Sensor 2 Motional Stark Effect
It is extremely important to minimize integration drift!
… or avoid it completely.
Inductive sensors require integration
Offline this is a simple process
Online it requires dedicated electronics
y=cos(x)
∫ y dx=sin(x)
+ 0.03
+ 0.03 x

## Slide 25: Real-time signal integration
Electronic integrators are typically used for real-time integration of the magnetic signals.
These work well for short discharges < 10 s
For longer discharges, this configuration requires precision electronics, complex and frequent calibration procedures.
Adjustments to hundreds of integrators for peak performance!
W7-X, a stellarator, intended to achieve pulses of 100s of seconds
Straight-up integration of sampled signal not feasible due to many DC offsets
But we can try to cancel them!
Wendelstein 7-X – A digital integration approach
A. Werner, Rev. Sci. Inst., 2006

## Slide 26: Digital integration with phase modulation
Periodic inversion of the coil signal before sampling
Elimination of the effect of drift inducing DC offsets added in the electronics chain
Enhanced long pulse performance due to low drift
Initially proposed for W7-X, adopted by ITER, implemented at ISTTOK, W7-X
A: Input signal
B: Chopper
C: Sampled
D: DC offset
E: Demodulated
F: Integrated
ADC module
Input filter
ADC
Signal conditioning
Chopper
FPGA
Demodulation
Integration
Decimation
A
C
E
F
B
D
Controller
Memory
Advantages
Low-drift integration
Mostly independent from precision analog electronics maintenance or ‘fidgeting’
Can be used as a normal DAS, by turning the switches off by software
Disadvantages
Demodulation artifacts
High dynamic range of magnetic signals
Requires strong filtering

## Slide 27: New generation modules and carrier
2-channel design
Input filter
Chopper
ADC 18bit @ 2 MSPS
Signal conditioning
Isolated power supply
Digital isolators
Two main components: Module carrier
FPGA (demodulation, integration)
Power distribution
PCIe over fiber
ATCA standard
48 modules
A. Torres, et al., “Data acquisition with real-time numerical integration for COMPASS-U magnetic diagnostics”, Fusion Engineering and Design 191, 113580, 2023
J Oliveira, A Torres, et al., Digitizer hardware for magnetic data acquisition on COMPASS-U, EPJ Web of Conferences 288, 03005, 2023
Modules
Analogue signal processing
Modulation
Digitization
Galvanic isolation
2 separate channels

## Slide 28: State-of-the-art drift performance
Requirement of 5 μVs/s for integrator drift on COMPASS-U
For comparison, the requirement for ITER is 500 μVs over 1h = 139 nV, 36 times more strict
Tests show a drift of |d| < 50 nVs/s for 90% of the cases (157 nVs/s max)
Great results not only on COMPASS-U timescales but also long pulses (>100 s)
While having high channel density, 20 kHz bandwidth, and modulation artifact reduction
CU
requirement
ITER
requirement
J. Oliveira, A. Torres, et al., " A real-time data acquisition system for the magnetic diagnostic of COMPASS-U" submitted to Plasma Physics and Controlled Fusion, 2026

## Slide 29: ELM buffering real-time controller

## Slide 30: Edge Localized Modes (ELMs)
MAST fast visible camera (A. Kirk, S. Lisgo, UKAEA)

## Slide 31: Edge Localized Modes (ELMs)
Energy deposited at the divertor
Permanent damage of the divertor tiles
Image: UKEA
J. W. Connor et al, 2008
1-1.5 MW/m2
Not sustainable for powerplant scenarios

## Slide 32: ELM buffering
ELM buffering:
Inject impurities to dissipate the ELM energy (radiation) before it reaches the divertor
Up to 3x reduction on energy deposited observed using Ar and N2 seeding
M. Komm, NF, 2023
Reference
Real-time Feedback System
Control the impurity ingress rate balancing power deposition and plasma performance.
N2 seeding
N2+Ar seeding

## Slide 33: How to detect ELM energy?
L. Giannone, 2024
Light from the Balmer lines (Hα or Dα) are the most commonly used signals to detect ELMs. However in arbitrary units.
With the Diamagnetic loop we can measure the drop in the plasma energy associated with the ELM
It was shown that thermoelectric currents in the divertor tiles can be used to estimate the thermal flux
By measuring the current with shunts we obtain a proxy for ELM energy at the divertor

## Slide 34: Real-time ELM detection
Upgrade of the DAS to 1 MSPS with real-time processing capabilities
Development of a real-time compatible algorithm for fast ELM detection and energy estimation
  Causal filter
  Differentiation and triggering on derivative
  Pre-trigger and debounce windows

## Slide 35: Real-time ELM detection
Upgrade of the DAS to 1 MSPS with real-time processing capabilities
Development of a real-time compatible algorithm for fast ELM detection and energy estimation
  Causal filter
  Differentiation and triggering on derivative
  Pre-trigger and debounce windows
Optimization of the detection parameters to minimize false positives and false negatives using independent statistical methods (Shapiro-Wilk test for normality)
Too low threshold, non-ELM events trigger
Too high threshold, many missed ELMs

## Slide 36: Real-time ELM detection
Upgrade of the DAS to 1 MSPS with real-time processing capabilities
Development of a real-time compatible algorithm for fast ELM detection and energy estimation
  Causal filter
  Differentiation and triggering on derivative
  Pre-trigger and debounce windows
Optimization of the detection parameters to minimize false positives and false negatives using independent statistical methods (Shapiro-Wilk test for normality)
Implementation on the Discharge Control System: the real-time distributed architecture at ASDEX-Upgrade in Munich
Work on the controller ongoing, with dedicated experiment planned for 2026
Front-end electronics for shunts
MTCA crate with fast DAS and RT processing
‘Old’ DAS for offline data acquisition
A. Torres, M. Komm, et al., "Real-time ELM energy estimation on ASDEX Upgrade", under preparation
Image: B. Sieglin et al, Fus. Eng. Des., 146 (2019)

## Slide 37: Key Takeaways
Despite extremely simple, the magnetic diagnostic provides vital important to the determination of the magnetic equilibrium, analysis of perturbations and control of the discharge
The magnetic diagnostic development for COMPASS-U was shaped by its unique challenges, specially high temperatures
Low drift integration is essential for future devices with longer discharges …
… in combination with non-inductive sensors
ELM mitigation is needed for high-power devices such as ITER and beyond
We are expanding the diagnostic capabilities of ASDEX-U, by having a real-time ELM energy monitor …
… that will be used for real-time ELM buffering control
Adapted from the XKCD comic
https://imgs.xkcd.com/comics/dependency.png
Some wires around the device
Physics exploitation on tokamaks and stellarators
Thank you for your attention!
Enabling controlled nuclear fusion – the role of magnetic diagnostics in tokamaks

## Slide 38: Backup slides

## Slide 39: First some context
Problem: End losses
Problem: Grad-B separates charges, creates E
Solution: Circular symmetry (torus)
Solution(s): Create helical field lines to average the separation to 0
USA: 3D field configuration
Image: PPPL
Figure of 8
Helical field lines
Image: IPP-MPG
Lyman Spitzer – Stellarator (1951)
Wendelstein 7-X (2015)

## Slide 40: The tokamak
Problem: Grad-B separates charges, creates E
Solution(s): Create helical field lines to average the separation to 0
USA: 3D field configuration
USSR: Add a poloidal field by driving current
Problem: Plasma current is also curved, so higher magnetic pressure on the inside pushes the plasma outwards
Andrei Sakharov and Igor Tamm proposed the tokamak in 1950, in secret.
Only fully shared with the international community at the Second Atoms for
Peace Conference in 1958
A. White 2015
J. P. H. Goedbloed and S. Poedts, 2004
Tokamak T1 (1958)
Solution: Vertical field -> J x B inward

## Slide 41: Plasma magnetic control
Current Position Shape
G. D. Tommasi, Journal of Fusion Energy, 2019
Isoflux
Gap
JET
DIII-D
NSTX-U

## Slide 42: Study of Mineral Insulated Cables
Fit of first order filter.
Greyed areas ignored in fit
Thinner sheath
Higher bandwidth
MIC from 0.5 to 3.2 mm diameter tested electrically and with induced fields.
Measurement of the attenuation of MIC flux loops against a non-MIC loop on COMPASS.
Data analysis: Spectrograms, power spectra through Welch method, fitting of first order filter.
A. Torres, et al., Mineral insulated cable assessment for inductive magnetic diagnostic sensors of a hot-wall tokamak, JINST, 2019

## Slide 43: Calibration and measurement of frequency response
A. Torres, et al., Mineral insulated cable assessment for inductive magnetic diagnostic sensors of a hot-wall tokamak, JINST, 2019
Torres, K. Kovarik et. al, Test bench for calibration of magnetic field sensor prototypes for COMPASS-U tokamak, Fus. Eng. Des., 168, 2021
Effective area calibration – Seff
  Long solenoid
  40 Hz – 1 kHz
Frequency response – g(f)
  Helmholtz coil
  <10 MHz (accurate to 1 MHz)
15m coax
cable element (x10)
Fast oscillation sensors: Measurement and modeling of the resonances introduced by the cables connecting to DAQ
MIC
non-MIC
Equilibrium sensors:
Quantification of the attenuation and delay introduced by metallic structures

## Slide 44: Mirnov coils development
Mirnov coils
Intended to detect fast perturbations better than MIC equilibrium coils
Limiting factor is the resonance introduced by the long (~ 30 m) cables
Same alignment method
In-kind contribution from PPPL, developed from the model used in NSTX-U

## Slide 45: MIC sensor prototyping and optimization
Signal simulation of COMPASS Mirnov coil with CU equilibrium coil response

## Slide 46: Qualification tests on COMPASS
We can recover digitally the attenuated high frequencies, provided the resolution is sufficiently high
This method is real-time compatible or can be applied in post-processing (as was the case) if the raw data is saved.
Detail on high frequency events recovered
Amplification of noise that is not subject to the input filter
Results published in [2]
[1] E. J. Strait, et. al, A hybrid digital–analog long pulse integrator, Rev. Sci. Instrum. 68 (1), 1997
[2] A. Torres, et al., “Data acquisition with real-time numerical integration for COMPASS-U magnetic diagnostics”, Fusion Engineering and Design 191, 113580, 2023

## Slide 47
Kirk, et al. PPCF, 2005