## Slide 1: Overview of IFJ PAN involvement in international projects
IFJ PAN - ESS technical meeting
Kraków, 24th March 2014
D. Bocian

## Slide 2: Outline
General information
Accelerator activities at IFJ
IFJ PAN and selected projects
  European XFEL
  LHC consolidation and upgrade
  Wendelstein 7X
Scientific equipment construction
Summary

## Slide 3: General information
530 personnel
Prof. 39, Assoc. Prof. 52, Ph.D. 108
PhD studies – 61 students
Interdisciplinary PhD studies
6 divisions: 28 departments
centre of excellence
centre of advanced technology
4 accredited laboratories
Equipment and Scientific Infrastructure Construction Division (DAI)

## Slide 4: Accelerator activities at IFJ
cyclotron AIC-144 - proton beam energy: 60 MeV - Proton Radiotherapy of Eye Melanoma
Cyclotron Proteus C-235
  National Centre for Hadron Radiotherapy
  under construction (2013)
neutron generator
  14 MeV
VdG high stability
  2.5 MeV

## Slide 5: IFJ PAN and international projects
Completed projects
  LHC, CERN Geneva, 2005 – 2012
  Wendelstein 7X, IPP Greifswald, 2007 – 2012
  ATLAS, CERN Geneva, 2004 - 2012
  T2K, J-PARC Tokai, Krakow/J-PARC, 2007 – 2009
Running projects:
  XFEL, DESY, Hamburg, 2009 – 2015
  LHC, CERN, Geneva, 2013 – 2014
  ITER, Cadarache, 2010-2015
  Cherenkov Telescope Array (CTA), 2008 – 2013

## Slide 6: IFJ PAN in-kind contribution to XFEL construction (2009 - 2015)
Performance of acceptance tests of cavities for a series of 840 units on DESY infrastructure and delivering the corresponding test reports
Performance of acceptance tests of cryomodules for a series of 103 units on DESY infrastructure and delivering the corresponding test reports
Performance of acceptance tests of cold magnets for a series of 103 units on DESY infrastructure and delivering the corresponding tests reports – common effort with DESY
XFEL quadrupole magnets tests
XFEL cryomodules tests
XFEL RF cavities tests

## Slide 7: IFJ PAN in-kind contribution to XFEL construction IFJ PAN tasks
Each IFJ PAN task is split in two phases:
Tests of cavities and cryomodules in the AMTF Hall
Tests of cold magnets
Serial tests phase
Performance of serial tests:
  Cold magnets – 100
  Current leads – 100
  Cavities – 816
  Cryomodules – 100
Data analysis and reporting;
Software upgrade.
Preparatory phase
Knowledge acquiring (learning, trainings, meetings with DESY experts);
Procedures writing;
Software preparation;
Performance of preseries tests:
(3 cold magnets and 3 CL,
24 cavities and 3 cryomodules).

## Slide 8: IFJ PAN in-kind contribution to XFEL construction IFJ PAN team structure
IFJ PAN Team
(Management)
Teams of cold magnets tests
(Technical Coordinator)
Measurement
Data Base and Software Development
Teams of cavities and cryomodules tests
(Technical Coordinator)
Mechanic
Vacuum
Cryogenic
RF Measurement
Software Development
Safety officer
Team:
Dr Engineers – 4
Engineers – 23
Technicians – 23
(currently at DESY
35 people)
Expertise:
Mechanics
Electronics / Electrics
Automatics / Robotics
Software engineering
Physics
Computer science

## Slide 9: IFJ PAN in-kind contribution to XFEL construction Cavity Test Flow chart
We create 3 reports from each test and upload them to the EDMS:
Incoming inspection report
Final test report
Outgoing inspection report

## Slide 10: IFJ PAN in-kind contribution to XFEL construction Cavity test: Incoming inspection & preparation for test
Main tasks:
Incoming Report
  Mechanical check of the cavity
  Vaccum check
  Electrical check
  Cavity spectrum check & HOM tuning
Assembling cavity to the insert
Connecting cavity to the vacuum line (in cleanroom conditions)
Cables connection with TDR
Leak check of the cavity
Transport of the insert to the cryostat
Connecting of the insert to the vacuum line

## Slide 11: IFJ PAN in-kind contribution to XFEL construction Cavity test: Cryogenic operation
Cryogenic activities at AMTF:
Cool down
Maintenance during the test
Warm up
Cool down process from 300 K to 2 K
Cryogenics operator’s control panel for test cryostat (left) and subcooler box (right) at AMTF.
Cavity cryostat at AMTF

## Slide 12: IFJ PAN in-kind contribution to XFEL construction Cavity test in vertical cryostat at 2K
Part of software written
by IFJ PAN engineers
Q vs E measurement
Cavity test-stand, cryostat (left) and electronic racks (right)
Cable calibration application
Vertical measurements application

## Slide 13: IFJ PAN in-kind contribution to XFEL construction Cavity test in vertical cryostat at 2K
Maximal Eacc (> 26 MV/m)
Q0 factor vs. Eacc (>1010)
Radiation vs. Eacc (<10-2 mGy/min)
Example of series cavities test results
Results overview from IFJ PAN cavitiy database

## Slide 14: IFJ PAN in-kind contribution to XFEL construction Cavity test: Disassembling and outgoing
Main tasks
Disconnecting of the insert from the vacuum line
Transport of the insert to the preparation area
Leak check of the cavity
Disconnecting cavity from the vacuum line (in cleanroom conditions)
Disassembling cavity from the insert
Outgoing check
  Mechanical check of the cavity
  Vacuum check
  Electrical check
  Cavity spectrum check
Preparation for shipment

## Slide 15: IFJ PAN in-kind contribution to XFEL construction Cavity test: Summary
Insertion of the cavity into the vertical cryostat
Results of RF cavity measurement
60 prototype and pre-series cavities – tested
800 production cavities - ~20% tested (end 2013)
Measurement of the cavity fundamental mode spectra

## Slide 16: IFJ PAN in-kind contribution to XFEL construction Cryomodule test: Incoming inspection and preparation for cold test
Incoming checks
  Mechanical check
  Vacuum check
  Check of the cavities fundamental mode spectra
  Electrical check
  Cavities tuner check
  Shock loggers readout
Load the cryomodule to the movable support
Assembling cryomodule at the test stand
Connecting cryomodule beam line to the test stand under clean room conditions
Leak check of beam line interconnections and mass spectroscopy of the beam line
Connecting of the waveguides and electrical cables
Connect of all cryomodule process pipes to the test stands
Leak check of cryomodule vessel (ISO-VAC) and cryogenic valves
Assembly and isolating thermal shields
Pumping down of vacuum insulation

## Slide 17: IFJ PAN in-kind contribution to XFEL construction Cold magnet test: Test-stand
Test stand for magnet tests at warm (top) and electronic rack (left).
Test stand for magnet tests at cold (top) and electronic racks (right)
CL electrical check test-stand
Hall 55 with cryogenic infrastructure for magnet tests

## Slide 18: IFJ PAN in-kind contribution to XFEL construction Cold magnet test: Preparation and cold test
Magnet with CL installation in cryostat XMTS
Electrical check of current leads connections
Thermal insulation CL and magnet
Results of stretched wire test at 2K
Stretched wire test at 2K

## Slide 19: IFJ PAN effort to XFEL construction
Total number of FTE’s over 7 years ~150
Total number of trained IFJ PAN staff ~ 60
Chart: [FTE]
| 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
 | 1.2 | 2.1 | 10.6 | 21.4 | 45 | 45 | 23

## Slide 20: IFJ PAN and LHC (2005-2014)
design & construction of measuring/testing devices
preparation of necessary software and data bases
manufacturing of superconducting N-lines
development of measuring/testing methods
organization, performance & documentation of electrical measurements /tests
organization, performance & documentation of interconnection inspection
Mobil test stations in LHC tunnel
Damaged PIM (Plug-In Module)
User interface

## Slide 21: IFJ PAN and LHC Summary
Just recently group of 25 people (engineers and technicians) from the IFJ-PAN was performing the reference measurements before consolidation of the LHC superconducting circuits during Long Shutdown 1. The measurements are now completed.
Exactly the same tests will be performed before machine start-up.
Currently we are monitoring to the circuits’ health during the consolidation.
Part of the team is working on investigation and solving of the nonconformities revealed during standard measurements: short circuits caused by thermal cycle, abnormal resistances, etc.
Chart: [FTE]
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
 | 18.7 | 33.7 | 38.2 | 9.8 | 11.3 | 1.7 | 2 | 2 | 29 | 23
Total number of FTEs over 8 years: ~160
Total number of trained IFJ PAN staff: ~50

## Slide 22: IFJ PAN contribution to W7-X construction (2007 – 2012)
IFJ PAN was responsible for the assembly of the bus bar system powering 70 superconducting coils on five modules of the stellarator.
The bus bars are made of the NbTi superconductors in an aluminium jacket.
There are 24 bus bars on each module.
Example of bus bars routing on one module
Total number of FTE over 6 years > 160
Total number of trained IFJ PAN staff > 50
Chart: FTE
| 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013
 | 3 | 18 | 45 | 43 | 36 | 19
Bus bar cross section

## Slide 23: IFJ PAN contribution to W7-X construction Joints assembly
Mechanical and electrical connection of the superconductors
Electrical connection of 81 triplets
Connected triplets squizzed with clamps and covered by stainless steel caps

## Slide 24: IFJ PAN contribution to W7-X construction Electrical insulation of joints (wet wrapping)
Electrical insulation of the assembled joints (divided into three steps)
All joints (184) passed successfully tightness and HV tests
Installation of 24 bus bars on the module
and final shaping of the bus bar ends
Module Separation Plane
set of six joints painted and clamped

## Slide 25: Scientific equipment construction Cherenkov Telescope Array (CTA)
Small Size Telescope Structure - prototype to be built by end 2013
dish diameter 4 m; focal length 9.6 m; weight 8.8 t
3-D model based on the technical documentation

## Slide 26: Scientific equipment construction Cherenkov Telescope Array (CTA)
Front (left) and rear (right) view of the prototype mirrors
Open structure mirrors for Medium Size Telescope – 10 prototypes under tests
hexagonal shape 1.2 m f-t-f, curvature radius 32 m, weight 35 kg

## Slide 27: Medical equipment construction Proton radiotherapy at IFJ PAN
Components of eye melanoma setup – to be finished in 2013
Device for immediate proton beam cut-off, so called shutter
Supports for the end of beam line
Adjustable supports for x-ray lamps
Holders for digital x-ray recorders
range discriminators and beam collimators

## Slide 28: Scientific equipment construction Finger detector at GSI Darmstadt
Mechanics for one detector – completed in 2012

## Slide 29: Scientific equipment construction Stellarator W7 - X
Mechanics for 30 sets of polychromators – completed in 2011

## Slide 30: Scientific equipment construction ATLAS Assembly
Aluminium frame to install Muon Chambers – completed in 2006
The frame at IFJ PAN
The frame used during installation in the ATLAS cavern

## Slide 31: Conclusions
IFJ PAN groups contribute to major world experiments in particle physics, astrophysics and nuclear physics.
IFJ PAN contributes to XFEL and LHC
IFJ PAN is involved in fusion projects (W7X, ITER)
Expertise:
    XFEL (construction)
    LHC (construction, consolidation, upgrade)
    W7-X (construction)
    AIC-144 (construction, medical applications)
    Proteus C235 (medical applications, research)
Team:
    Scientists: 5
    Engineers: 34
    Technicians: 65